Advantages of BLE:

- Less power consumption.
- Used for less data applications so that it can run on a small battery for more than 1 year.
- BLE power consuption,a compatibility with Bluetooth LE could be cheaply added to devices which support Classic Bluetooth.
- Device monitoring and Real time positioning Services: BLE devices have the capacity for location intelligence and real-time tracking of whether an asset in within the premises, which can be tracked using a smartphone.
- Robust radio – designers can target a line-of-sight range of as much as 100m. A frequency-hopping scheme makes a Bluetooth LE radio highly resistant to interference at its 2.4GHz licence-free band.
- Range & channels: The Bluetooth frequency range is actually 2,400MHz – 2,483.5MHz. In the case of Bluetooth LE, this frequency band is split into 40 channels with 2MHz spacing, whereas Classic Bluetooth uses 79 channels with 1MHz spacing.
  Range : 100 meters ( Increased modulation index ). Range may vary depending on implementation.
  Enhanced range : optimize range to 200 feet and beyond.
- Lower implementation costs.
- An ability to communicate between systems, and share data between systems.
- Data Transfers : 8 octet minimum up to 27 octets of packet maximum.
- Speed : 1 Mbps.
- It will be possible to have sensors operating continuously, and intermittently communicating with other devices like a mobile phone.
Versions of BLE:

BLE is introduced from Bluetooth 4.0.The versions of BLE are 4.1,4.2.Bluetooth 4.2 is an important update to the Bluetooth Core Specification with many new features and benefits designed specifically for Bluetooth Smart technology, and advantages when comparing Bluetooth 4.2 vs. Bluetooth 4.1 (also known as Bluetooth Low Energy or Bluetooth Smart).

Bluetooth 4.2 introduces several new features that improve speed and privacy over Bluetooth 4.1 but the main advantage is allowing chips to use Bluetooth over Internet Protocol version 6 (IPv6) for direct Internet access.

We use BLE 4.2 instead of BLE 4.1 because Bluetooth SIG recommends implementing Bluetooth 4.2 in all new designs and requires the same qualification process as all other Bluetooth designs. Devices using Bluetooth Smart will be backward compatible with Bluetooth 4.0 or 4.1 devices that also implement the low energy features.
IoT Capabilities:
    Low-power IP (IPv6/6LoWPAN)
    Bluetooth Smart Internet Gateways (GATT)

With BLE 4.2 Bluetooth Smart sensors can transmit data over the internet.

Security:

    LE Privacy 1.2
    LE Secure Connections

With new, more power efficient and highly secure features, BLE 4.2 provides additional benefits allowing only trusted owners to track device location and confidently pair devices.

Speed:

    250% Faster
    10x More Capacity

Compared to previous versions, BLE 4.2 enables 250% faster and more reliable over-the-air data transmission and 10x more packet capacity.